## Slide 1: Fundamentals of Computer Networks and Management
Atul Kahate

## Slide 2: Sessions 1 and 2

## Slide 3: Electronic Communication System

## Slide 4: Introduction to Communication System
Communication system allows exchange of data between two stations, transmitter and receiver
Signals pass from source to destination through what is called channel, which represents a way that signal use it to move from source toward destination
To transmit signals in communication system, it must be first processed in several stages, beginning from signal representation, to signal shaping until encoding and modulation
After preparing the transmitted signal, it is passed to the transmission line of channel
Due to the signal crossing this media it faces many impairments such as noise, attenuation and distortion

## Slide 5: Components of a Data Communication System
Transmission device or Sender
  A device that actually sends out the message.(eg computer , telephone, etc).
A medium
  A physical channel where the information travels from the sender to the receiver.
Message
  The data/information to be transmitted. It can be in the form of text, audio, video, photos, or combination of them.
Receiving device or Receiver
  A device that receives the message then process the information in the message.

## Slide 6: Issues in Computer Networking
Sharing computer resources
  Interaction between computers
  Network applications
Physical data transmission
  Encoding
  Physical link characteristics
Interaction among several computers
  Topology
  Addressing
  Switching

## Slide 7: Network Hardware and Software
Two types of transmission technology: Broadcast links and Point-to-point links
Broadcast network
  The communication channel is shared by all the machines on the network
  Packets sent by any machine are received by all the others.
  An address field within each packet specifies the intended recipient.
  A wireless network is a common example of a broadcast
Point-to-point network
  Links connect individual pairs of machines
  Point-to-point transmission with exactly one sender and exactly one receiver is sometimes called unicasting

## Slide 8: Unicast versus Broadcast

## Slide 9: Scale and Network Types

## Slide 10: Local Area Network (LAN)
Local Area Network (LAN): A privately owned network that operates within a single building like a home, office or factory
Wireless LANs: In these systems, every computer has a wireless modem and an antenna that it uses to communicate with other computers
  An access point or base station controls the network
  IEEE 802.11 standard (also called WiFi) describes this

## Slide 11: Network Topology
Network Topology represents a network arrangement consisting of several nodes

## Slide 12: Bus Topology
All the nodes are connected to a common wire, called as bus
Simple and cost-effective, but all depends on a single cable, not fast

## Slide 13: Ring Topology
One computer is connected to the next, and so on, to complete a ring
A transmitting computer needs to have a token, before transmitting
Inexpensive, Tough to add or remove nodes, One node crashing can disconnect the whole network

## Slide 14: Star Topology
Each device is connected to a central hub
All communication goes through the hub only
Simple, too much of dependence on the hub, but the hub can be upgraded easily, Easy to troubleshoot, Cost is high

## Slide 15: Mesh Topology
All nodes are connected to each other
Point-to-point connection, so for n nodes: links
Very robust, Easy to diagnose errors, Privacy and security are better, Costly, Too much of wiring

## Slide 16: Tree Topology
Nodes are connected hierarchically, ultimately connecting to the top node, called as the root node
Has at least three levels of hierarchy
Easy to expand and manage, debug
Expensive, lot of cabling

## Slide 17: Network Interface Card (NIC)

## Slide 18: Transmission media

## Slide 19: Transmission media

## Slide 20: Transmission Media
Transmission medium: Carries information from a source to a destination
Guided media (Wired) include twisted-pair cable (uses electric current), coaxial cable (uses electric current), fiber-optic cable (uses light)
Unguided medium (Wireless) is air

## Slide 21: Twisted-pair cable
Consists of two copper wires
Two types
  Unshielded twisted-pair (UTP)
  Shielded twisted-pair (STP)
Used in telephone networks

## Slide 22: Coaxial cables
Coaxial cable (or coax) carries signals of higher frequency ranges than those in twisted-pair cable
Instead of having two wires, coax has a single copper wire
Usage: Telephone, Cable TV, LAN

## Slide 23: Fiber-optic cable
Made of glass or plastic and transmits signals in the form of light
Modern Ethernet is fiber optic-based

## Slide 24: Unguided media
Use electromagnetic waves – no wire is needed
Also called as wireless communication
Signals are normally broadcast through free space and thus are available to anyone who has a device capable of receiving them
The part of the electromagnetic spectrum, ranging from 3 kHz to 900 THz is used for wireless communication.

## Slide 25: Ethernet
Most popular LAN technology
Earlier, we also had Token Ring, Token Bus, etc
Ethernet generations
  Standard Ethernet (10 Mbps)
  Fast Ethernet (100 Mbps)
  Gigabit Ethernet (1 Gbps)
  10 Gigabit Ethernet (10 Gbps)

## Slide 26: Earlier Ethernet – Classic Ethernet
Carrier sense multiple access with collision detection (CSMA/CD) technique was used
Allow any host to send data
If two hosts transmit at the same time, collision happens
They recover using CSMA/CD

## Slide 27: CSMA/CD

## Slide 28: Modern Ethernet: Switched Ethernet
Devices called switches are used to connect different computers
Classic Ethernet is the original form and ran at rates from 3 to 10 Mbps
Switched Ethernet
  Fast Ethernet: 100 Mbps
  Gigabit Ethernet: 1000 Mbps (1 Gbps)
  10 Gigabit Ethernet: 10,000 Mbps (10 Gbps)
In practice, only switched Ethernet is used nowadays

## Slide 29: Switched Ethernet
Hosts connect into switches, and switches connect to each other
Ethernet switch

## Slide 30: LAN – Earlier and Now

## Slide 31: Wide Area Network (WAN)
A Wide Area Network (WAN) spans a large geographical area, often a country or continent
Example: Two LANs can be connected to form a WAN

## Slide 32: Sessions 3 and 4

## Slide 33: Protocol
Communication between two people or two devices needs to follow some protocol
A protocol is a set of rules that governs communication
For example, in a face-to-face communication between two persons, there is a set of implicit rules in each culture that define how two persons should start the communication, how to continue the communication, and how to end the communication

## Slide 34: Network Software
Network software uses a protocol stack
A protocol stack contains many layers or levels
Each layer provides some services to the layer above it
Each layer hides complexity of its work from the layer above it
Creates a protocol hierarchy

## Slide 35: Protocol Hierarchy Example

## Slide 36: OSI
Open Systems Interconnection
Good in theory, not used in practice
Contains 7 layers
Sometimes also called ISO/OSI

## Slide 37
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Layers in OSI
Notes: 37

## Slide 38: An Exchange using the OSI Model

## Slide 39: The Application Layer

## Slide 40: Application Layer
Provides an “application view” to a network (e.g. email, file transmission)
Example: Hypertext Transfer Protocol (HTTP) is used to access Web pages
Encapsulation begins here
Other examples: Email (SMTP), File transfers (FTP), Querying domain names (DNS)

## Slide 41: The Presentation Layer

## Slide 42: Presentation Layer
Translation: Use of a common format to take care of differences (encoding, number representation etc)
Encryption: To achieve confidentiality or privacy
Compression: Reduces the number of bits needed to be transmitted

## Slide 43: The Session Layer

## Slide 44: Session Layer
Manages the session between applications
Example: Between browser of the source computer and server of the destination computer

## Slide 45: The Transport Layer

## Slide 46: Transport Layer
Identifies the application on the destination computer using port numbers
Example: One server, multiple applications

## Slide 47: Port Numbers
Port number is a 16-bit value, so it can store a number between 0 and 65,535
Port Number Range | Where used? | Called as
0-1023 | Server | Well-known ports
1024-49151 | Client | Temporary/Ephemeral
49152-65535 | NA | Dynamic, Usage-based

## Slide 48: The Network Layer

## Slide 49: Network Layer
Physical/MAC addresses are defined by data link layer to take care of addressing inside the same network
If a packet has to travel across a network to another network, physical addressing will not work
Hence, a universal address or a logical address is required. This is done at the network layer
This is the IP address

## Slide 50: The Data Link Layer

## Slide 51: Data Link Layer
Responsible for delivery of packets between two hosts connected to the same physical network (hop-to-hop – see next slide)
  Cannot work across networks
Uses frames
Physical addressing: Adding sender’s and receiver’s physical addresses (also called MAC addresses) to the frame header
LAN/WAN operates at this layer (e.g. Ethernet or WiFi)
What if we know the IP address of a computer but do not know its MAC address?
  Use Address Resolution Protocol (ARP)

## Slide 52: The Physical Layer

## Slide 53: Physical Layer Functions
Carries the data (0s and 1s) in the form of signals
Signals can be electric, optical, or wireless

## Slide 54: Physical and Logical Address
Each computer on the Internet has two addresses:
Physical address/MAC address/Hardware address
  Fixed address, hardcoded on the Network Interface Card (NIC)
  Different for different network type (e.g. Ethernet card, WiFi card)
  Useful within or inside a network only
Logical address/IP address/Virtual address
  Exists in software
  Given by the network provider or your organization (usually temporary)
  Useful outside a network (e.g. to reach another computer on the Internet, anywhere in the world)

## Slide 55: Example

## Slide 56: Example
Suppose we have used our web browser to access a web page located on our company’s web server
Consider that the following are the details of the two computers
Computer | IP Address | MAC Address | Port Number
Web server | 192.168.5.1 | 5-5-5-5-5-5 | TCP 80
Laptop | 192.168.5.2 | 6-6-6-6-6-6 | TCP 5091

## Slide 57: How will the Web Server Respond?
Layer 7 obtains the data in the form of the HTML document.
Layer 6 adds information about the formatting.
Layer 5 adds information required to create a session between the web server and the web browser on the laptop.
Layer 4 adds the transport protocol and the source and destination port numbers, in this case TCP (it's a unicast) and port 80 (HTTP).
Layer 3 adds the source and destination IP addresses, in this case a source of 192.168.5.1 and a destination of 192.168.5.2.
Layer 2 learns the destination MAC address and adds the source and destination MAC addresses, in this case, a source of 5-5-5-5-5-5 and destination of 6-6-6-6-6-6.
Layer 1 converts the entire package into bits and sends it across the network to the laptop.

## Slide 58: How will the Laptop Handle this?
Layer 1 receives the bits in electrical format, converts them to be read by layer 2, and hands them to layer 2.
Layer 2 examines the destination MAC address to see whether it is addressed to it, sees the MAC address of 6-6-6-6-6 (its own), drops that part of the transmission, and hands the remaining data to layer 3.
Layer 3 examines the destination IP address to ensure that it is its own (192. 168.5.2), drops that part, and hands the rest of the package to layer 4.
Layer 4 examines the destination port number (port 5091), alerts the browser that HTTP data is coming in, drops that part, and hands the rest of the package to layer 5.
Layer 5 uses the information that was placed on this layer by the web server to create the session between the web server and the web browser and then hands the rest of the information to layer 6.
Layer 6 performs any format translation that may be required and hands the remaining data (the HTML document) to layer 7.
The layer 7 application (the web browser) receives the HTML document and opens the document in the browser window.

## Slide 59: TCP/IP

## Slide 60: Basics of TCP/IP
The TCP/IP protocol suite was developed prior to the OSI model
Therefore, the layers in the TCP/IP protocol suite do not match exactly with those in the OSI model
The original TCP/IP protocol suite was defined as four software layers built upon the hardware
Sometimes TCP/IP is thought of as a five-layer model with the layers named similarly to the ones in the OSI model

## Slide 61: OSI versus TCP/IP
When we compare the two models, we find that two layers, session and presentation, are missing from the TCP/IP protocol suite
These two layers were not added to the TCP/IP protocol suite after the publication of the OSI model
The application layer in the suite is usually considered to be the combination of three layers in the OSI model
See diagram on the next slide

## Slide 62: OSI versus TCP/IP

## Slide 63: Protocols within Each TCP/IP Layer

## Slide 64: Transport Layer Protocols
Transmission Control Protocol (TCP)
  Reliable protocol
  Guaranteed delivery
  Uses connections, acknowledgements
  Used for text-based data
User Datagram Protocol (UDP)
  Unreliable protocol
  No guarantee of delivery
  No connections, no acknowledgements
  Useful for audio, video or wherever we need speed but not guarantee

## Slide 65: TCP – Connection Management
Connection establishment
Data transfer
Connection termination

## Slide 66: UDP
No connection
No acknowledgement
No retransmissions in the case of errors

## Slide 67: Internet Layer
Provides logical addressing (IP addresses)
Performs routing
Provides an IP datagram format (See next slide)

## Slide 68: IP Datagram Format

## Slide 69: Session 8-10: Network Devices – Hub, Switch, and Router

## Slide 70: Networking devices
Inside a network
  Hub: Older device
  Switch: Modern device
To connect different networks
  Router

## Slide 71: Hub
Earlier, hubs were used as connection devices in Ethernet
Hub is a dumb device, works only at the physical layer (Layer 1).
So, it does not know about MAC addresses, and hence floods out all the ports.
Hub operates only in half duplex mode
  Attached hosts cannot send and receive data at the same time – they can perform only one of the tasks
  All devices in a hub share the same collision domain – If two or more devices transmit at the same time, collisions will occur, leading to CSMA/CD

## Slide 72: Collision domain concept
All devices that use the same physical media and listen to each frame are considered to be in the same collision domain.
This means that only one device can transmit at any given time, and any other device on the network segment must synchronize with the signal and extract the frame.

## Slide 73: Hub

## Slide 74: Switch
Hubs are obsolete
Switch is an intelligent device – can filter traffic
Example
  If a hub connects two branches of a network, it will flood both the branches for every received frame
  A switch will check whether it should send it to the other branch of the network by comparing addresses, as discussed shortly

## Slide 75: More on Switch
From the outside, a switch looks just like a hub.
They are both boxes, typically with 4 to 48 ports, each with a standard RJ-45 connector for a twisted-pair cable.
If the switch itself fails, it will need to be replaced.

## Slide 76: Multiple switches are used these days (Not hubs) …

## Slide 77: Switching Example – 1
Each switch maintains a mapping table

## Slide 78: Switching Example – 2
Host 1.1.1 sends a frame to host 2.2.2
Switch sees the frame and updates its mapping table
The switch does not know where 2.2.2 is, so it floods out the frame
`

## Slide 79: Switching Example – 3
Suppose host 2.2.2 sends a reply to 1.1.1
Switch sees the frame and updates its mapping table
The switch will send the frame only to 1.1.1

## Slide 80: “Layer 2” Switch
In OSI, data link layer is layer 2 from the bottom
A switch operates at the data link layer
Hence, sometimes it is also called as Layer 2 switch

## Slide 81: Router
Routers know the paths to get to the different IP subnets on network
They are required to send traffic from one subnet to another
They are also required to send traffic from one network to another
Routers operate at Layer 3 of the OSI model (network layer)

## Slide 82: Routers versus Switches
Routers are Layer 3 aware and can route traffic between different networks
Switches are Layer 2 aware and can switch traffic between hosts on the same LAN
Routers support many types of interfaces, such as Ethernet, Serial ISDN, ADSL etc
Switches typically only support Ethernet interfaces
Switches will typically have more ports than routers

## Slide 83: Switch Operation

## Slide 84: Router Operation

## Slide 85: Understanding Routing
Consider a passenger traveling from Pune to Sioux Falls, USA
Hop Number | From | To | Passenger’s View
1 | Pune | Mumbai | Pune-Sioux Falls
2 | Mumbai | San Francisco | Pune-Sioux Falls
3 | San Francisco | Chicago | Pune-Sioux Falls
4 | Chicago | Sioux Falls | Pune-Sioux Falls
Pune
Mumbai
San Francisco
Chicago
Sioux Falls

## Slide 86: Understanding Routing
Consider a datagram/packet going from computer A to computer B
R1
R2
R3
A
B
 | Data Link Layer | View | 
Hop Number | From | To | IP View
1 | A | R1 | A-B
2 | R1 | R2 | A-B
3 | R2 | R3 | A-B
4 | R3 | B | A-B

## Slide 87: MAC Addresses and LAN

## Slide 88: IP Addresses and the Internet

## Slide 89: Address Resolution Protocol (ARP)
Takes IP address of a computer as input and finds the MAC address of that computer
Useful to deliver the data to a particular MAC address

## Slide 90: ARP Example

## Slide 91: Internet Message Control Protocol (ICMP)
IP is
  Connectionless
  Unreliable
  Unacknowledged
Datagrams are sent over the Internet with no prior connection, no assurance of delivery, and no acknowledgement if they reach the destination successfully
What happens if a router must discard a datagram because it cannot find a router to the final destination, or because the time-to-live field has a zero value?
What happens if the final destination host must discard all fragments of a datagram because it has not received all fragments within a predetermined time limit?
The Internet Control Message Protocol (ICMP) helps IP

## Slide 92: ICMP Message Types
Error-reporting messages
  Report problems that a router or a host (destination) may encounter when it processes an IP packet
Query messages
  Occur in pairs, help a host or a network manager get specific information from a router or another host.
  For example, nodes can discover their neighbors.
  Also, hosts can discover and learn about routers on their network and routers can help a node redirect its messages.

## Slide 93
ICMP Messages
Notes: 93

## Slide 94: ICMP Message Format
Has a 8-byte header and variable-size data section
General format of the header is different for each message type, the first 4 bytes are common to all
Specifies the reason for the specific message type
Defines the type of the message
Carries information for finding the original packet that had error

## Slide 95
Example: Destination Unreachable
When a router cannot route an IP datagram, it sends this message
Notes: 95

## Slide 96
Destination Unreachable – Sample ‘Code’ field Values
Code 0: Network is unreachable
Code 1: Host is unreachable
Code 2: Protocol is unreachable (e.g. TCP is not running on the destination)
Code 3: Port is not reachable
Code 4: Fragmentation is needed, but “Do not fragment” field is set
Code 6: Destination network is unknown
Code 7: Destination host does not exist
Notes: 96

## Slide 97: Dynamic Host Configuration Protocol (DHCP)
Need for DHCP
Computers have permanent MAC addresses, but generally dynamic IP addresses
  Static IP addresses need to be manually configured by the administrator
Example: People using their own devices, mobile phones needing Internet connectivity, Accessing the Internet at home and in the office
DHCP concept
  An organization or the network service provider sets up a DHCP server
  A device needing an IP address contacts the server, and asks for an IP address
  The server allocates an IP address to the computer for a specific duration

## Slide 98: DHCP Flow

## Slide 99: Sessions 6 and 7: IP Addressing and Routing

## Slide 100: IP Address
An IP address has two parts:
  Network Id: Identifies which network it belongs to
  Host Id: On a given network, what is the host number
Examples:
This notation is called as dotted decimal notation
Some portion of the network id is reserved to indicate class of IP address
Hence, this is called as classful addressing
14.22.130.89
143.1.99.204
193.56. 78.21

## Slide 101: Classful Addressing

## Slide 102: Classes – How to Determine/Remember? – Three Techniques
Look at the first few bits of the binary value of the network id
  First bit 0: Class A
  First two bits 10: class B
  First three bits 110: class C
Look at the first decimal octet/byte value of the network id
  0-127: Class A
  128-191: Class B
  192-223: Class C
Use the flow-chart on the following slide

## Slide 103
Determining Class
First bit = 0?
Second bit = 0?
Third bit = 0?
Fourth bit = 0?
Yes
Yes
Yes
Yes
No
No
No
No
Class A address
Class B address
Class C address
Class D address
Class E address
Notes: 103

## Slide 104: Dotted Decimal Notation

## Slide 105: Another View

## Slide 106
IP Addresses Allocation to Classes
Notes: 106

## Slide 107
Exercise
How many addresses can each of the classes have?
Notes: 107

## Slide 108
Addresses Per Class
Class | Number of Addresses | Percentage
A | 20 Lakh | 50%
B | 10 Lakh | 25%
C | 5 Lakh | 12.5%
D | 2.5 Lakh | 6.25%
E | 2.5 Lakh | 6.25%
Notes: 108

## Slide 109
Exercise
Find the class of the following addresses
227.12.14.87
193.14.56.22
14.23.120.8
252.5.15.111
134.11.78.56
Notes: 109

## Slide 110
Determining Class Based on an IP Address
Class | Contents of First Byte (Last three are not shown)
A | 1 to 126 (0 and 127 are reserved)
B | 128 to 191
C | 192 to 223
D | 224 to 239
E | 240 to 255
Notes: 110

## Slide 111
Masking
Given the IP address of a host, can we find its network address?
  “Masking” concept: AND the complete IP address with a “Mask”, result is the network address
Notes: 111

## Slide 112
Masking concept
If IP address is 134.45.78.2, network ID is 134.45
An address in the block
Mask
AND
Network portion of the IP address
Notes: 112

## Slide 113
Masking Example
If IP address is 134.45.78.2, network ID is 134.45 (See next slide)
134.45.78.2
255.255.0.0
AND
134.45
Notes: 113

## Slide 114: Calculation
134.45.78.2
255.255.0.0
AND
134.45.0.0
The address whose network ID we want
Default mask for class B (since the address above is from class B)
Network ID for the address

## Slide 115: Default Mask

## Slide 116
Default Masks
Class | Mask in Binary | Mask in dotted-decimal
A | 11111111 00000000 00000000 00000000 | 255.0.0.0
B | 11111111 11111111 00000000 00000000 | 255.255.0.0
C | 11111111 11111111 11111111 00000000 | 255.255.255.0
Notes: 116

## Slide 117
Masking Examples
Given an IP address of 23.56.7.91, find the network address.
Given an IP address of 132.6.17.85, find the network address.
Notes: 117

## Slide 118: Private/Local/Internal IP Addresses
The following ranges of IP addresses are reserved as private/local/internal IP addresses, and they cannot be assigned to a computer on the Internet as a public/external IP address
Class A: 10.0.0.0 to 10.255.255.255
Class B: 172.16.0.0 to 172.31.255.255
Class C: 192.168.0.0 to 192.168.255.255

## Slide 119: Subnetting
Notes: 119

## Slide 120: Subnetting Concept

## Slide 121
Subnet Concept
Two ways to address a particular house
  Building number, House number (Normal IP address)
  Building number, Floor number, House number (IP address with subnet)
Network id
Host id
Network id
Host id
Subnet id
Notes: 121

## Slide 122
Subnetting
Divide a network into smaller sub-networks with each subnet having its own IP address
  Allow a network to be split into several internal sub-networks, but act like a single network to the outside world
Motivation: Make better use of the IP address space
IP addresses: Two levels of hierarchy; subnetting makes it three
Notes: 122

## Slide 123: Subnetting Example
Consider a network having IP address 200.1.2.0
We want to divide this into two parts, creating two subnets
Analysis: Network belongs to class C

## Slide 124: Subnetting Example
We want to create two subnets
Subnet 1 will have id 02
Subnet 2 will have id 12
IP address length is always 32 bits
For the current example, we have:
  Net id: 24 bits
  Host id: 8 bits
We need one bit for the subnet id: From where to take, and why?

## Slide 125: Subnetting Example
If we take 1 bit from the net ID
  Net id will become 23 bit
  What will be the impact?
  Current net ID is:
  Which bit to take?
    Suppose we take the last bit in the third octet (i.e. 0)
      Now net ID will become 200.1.1 (because last octet will now be of only 7 bits 0000001)
    Suppose we take the first bit in the first octet (i.e. 1)
      Now net ID will become 72.1.1 (because first octet will now be of only 7 bits 1001000)
Conclusion: We cannot touch the net ID
200 | 1 | 2
11001000 | 00000001 | 00000010

## Slide 126: Subnetting Example
Conclusion: We must take one bit from the host id
This bit must be from the leftmost part of the host id
Now, the host id will only have 7 bits
If borrowed bit = 0, then it represents the first subnet
If borrowed bit = 1, then it represents the second subnet

## Slide 127: Resulting Subnets
IP addresses of the two subnets:
200.1.2.00000000 = 200.1.2.0
200.1.2.10000000 = 200.1.2.128

## Slide 128: Subnet 1
Network address of the subnet = 200.1.2.0
Total number of IP Addresses = 27 = 128
Total number of hosts that can be configured = 128 – 2 = 126
Range of IP Addresses = [200.1.2.00000000, 200.1.2.01111111] = [200.1.2.0, 200.1.2.127]
Broadcast Address = 200.1.2.01111111 = 200.1.2.127

## Slide 129: Subnet 2
Network address of the subnet = 200.1.2.128
Total number of IP Addresses = 27 = 128
Total number of hosts that can be configured = 128 – 2 = 126
Range of IP Addresses = [200.1.2.10000000, 200.1.2.11111111] = [200.1.2.128, 200.1.2.255]
Direct Broadcast Address = 200.1.2.11111111 = 200.1.2.255

## Slide 130: Exercise
Consider that we have a single network having IP Address 200.1.2.0
We want to do subnetting and divide this network into 4 subnets

## Slide 131: Solution
The network belongs to class C
To create 4 subnets, we need 2 bits from the host id to be used as subnet id
Host id will now have 6 bits
Subnet IDs
  Subnet ID 1: 00
  Subnet ID 2: 01
  Subnet ID 3: 10
  Subnet ID 4: 11

## Slide 132: Solution
IP addresses of the four subnets
200.1.2.00000000 = 200.1.2.0
200.1.2.01000000 = 200.1.2.64
200.1.2.10000000 = 200.1.2.128
200.1.2.11000000 = 200.1.2.192

## Slide 133: Subnet 1
Network Address of the subnet = 200.1.2.0
Total number of IP Addresses = 26 = 64
Total number of hosts that can be configured = 64 – 2 = 62
Range of IP Addresses = [200.1.2.00000000, 200.1.2.00111111] = [200.1.2.0, 200.1.2.63]
Broadcast Address = 200.1.2.00111111 = 200.1.2.63

## Slide 134: Subnet 2
Network Address of the subnet = 200.1.2.64
Total number of IP Addresses = 26 = 64
Total number of hosts that can be configured = 64 – 2 = 62
Range of IP Addresses = [200.1.2.01000000, 200.1.2.01111111] = [200.1.2.64, 200.1.2.127]
Broadcast Address = 200.1.2.01111111 = 200.1.2.127

## Slide 135: Subnet 3
Network Address of the subnet = 200.1.2.128
Total number of IP Addresses = 26 = 64
Total number of hosts that can be configured = 64 – 2 = 62
Range of IP Addresses = [200.1.2.10000000, 200.1.2.10111111] = [200.1.2.128, 200.1.2.191]
Broadcast Address = 200.1.2.10111111 = 200.1.2.191

## Slide 136: Subnet 4
Network Address of the subnet = 200.1.2.192
Total number of IP Addresses = 26 = 64
Total number of hosts that can be configured = 64 – 2 = 62
Range of IP Addresses = [200.1.2.11000000, 200.1.2.11111111] = [200.1.2.192, 200.1.2.255]
Broadcast Address = 200.1.2.11111111 = 200.1.2.255

## Slide 137: Subnetting Exercise
For an address 192.168.5.85 /24, we want to create 5 subnets.
What will be the first host address on the first subnet and the second host address on the second subnet?
How many hosts are possible per subnet?

## Slide 138: Solution
Our network address is 192.168.5.85 /24.
We want to create 5 subnets. So, 3 bits from the host id portion will be used for the subnet id. So, 5 bits will be left for the host id.
First subnet id in binary will be: 000
First address possible in the first subnet will be: 00000. But this is not the first host address, as this is reserved as the first subnet address.
So, the first host address within the first subnet will be 00001.
The first host address within the first subnet will be:
192.168.5.(000 00001) to the base 2
192.168.5.1 - First host address in the first subnet
The second host address within the second subnet will be:
192.168.5.(001 00010) to the base 2
192.168.5.34
Number of hosts per subnet = 2h – 2 = 25 – 2 = 30

## Slide 139: Subnetting Exercise – 3
Consider a class C network with IP address 198.34.5.0.
You are asked to create 6 subnets.

## Slide 140: Solution
(1) Write the default mask in decimal.
=> 24 bits are reserved for the network id, 8 bits are reserved for the host id
So, the default mask will be 255.255.255.0
(2) Write the subnet mask in decimal.
=> We want to create 6 subnets. For 6 subnets, we will need to reserve 3 bits for the subnet id (because 2 to the power 3 = 8, which is >= 6)
As we know, the default mask is 255.255.255.0 in decimal
In binary, it will be 11111111.11111111.11111111.00000000
Subnet mask will be: 11111111.11111111.11111111.11100000
Subnet mask in decimal will be: 255.255.255.224
(3) Write the subnetted address for this network.
=> Default network address for this network is 198.34.5.0/24.
Subnetted address for the same network will be 198.34.5.224/27.
(4) What will be the first host address of the first subnet in this network?
=>
There are 6 subnets.
3 bits are reserved for the subnet id.
Subnet ids will be:
First subnet id: 000
Second subnet id: 001
Third subnet id: 010
...
Eigthth subnet id: 111
From above, the first subnet id is 000.
Within this first subnet, the first possible address is 00000
However, the first address is any network or in any subnet is reserved as the network address.
Thus, the first host address will be 00001.
Thus, the full address for the first host in the first subnet will be 00000001 in binary, or 1 in decimal.
And its complete IP address will be 198.34.5.1/27.
(5) How many hosts are possible in the third subnet? What will be the network address for the third subnet, what will be the first host address for the third subnet, and what will be the last host address for the third subnet?

## Slide 141: Subnetting Exercise – 4
What are the network address, broadcast address, and valid host addresses for the IP address 198.22.45.173/26?
What is the subnet mask in dotted decimal notation?

## Slide 142: Solution
Let’s figure out the subnet mask in dotted decimal notation first because that’s easy...
/26 borrows the first 2 bits in the last octet
128 + 64 = 192
So the subnet mask is 255.255.255.192

## Slide 143: Solution - Subnets and Hosts
Our given address is 198.22.45.173/26
Since two bits are reserved for the subnet id, 4 subnets 00, 01, 10, and 11 are possible
We need to think “Our IP address will fall in which of these four subnets?”
To answer this, let us calculate the address range for each of the four subnets

## Slide 144: Solution - Subnets and Hosts
Our given address is 198.22.45.173/26
Subnet Number (Decimal) | Subnet ID (Binary) | First full address in the subnet (Binary) | Last full address in the subnet (Decimal) | First full address in the subnet (Binary) | Last full address in the subnet (Decimal) | Our target IP address (173)
1 | 00 | 00000000 | 00111111 | 0 | 63 | Not here
2 | 01 | 01000000 | 01111111 | 64 | 127 | Not here
3 | 10 | 10000000 | 10111111 | 128 | 191 | Here
4 | 11 | 11000000 | 11111111 | 192 | 255 | Not here

## Slide 145: Solution
Next let’s calculate the address range for this subnet
The network portion of the address is the first 26 bits
198.22.45.128 is the network address (First address of the third subnet – See the previous slide)
The line is after 64, so add 64 to get the network address of the next subnet
The next subnet begins at 198.22.45.192
So the broadcast address is 198.22.45.191
And the valid host addresses are 198.22.45.129 to 198.22.45.190

## Slide 146: Summary: Subnetting in Class C

## Slide 147: Variable Length Subnet Mask (VLSM)

## Slide 148: VLSM Concept
Early routing protocols only supported Fixed Length Subnet Masking (FLSM) where all subnets had to be the same size.
You couldn’t have a subnet with 14 hosts and another subnet with 64 hosts in the same network.
All modern routing protocols support Variable Length Subnet Masking (VLSM).
This allows us to size subnets differently according to how many hosts they have.

## Slide 149: VLSM Considerations
How many locations do we have in the network?
How many hosts are in each location?
What are the IP addressing requirements for each location? (Should different departments or types of host be in different subnets?)
What size is appropriate for each subnet? (Don’t waste addresses, but leave room for growth.)

## Slide 150: VLSM Example
Suppose there is an administrator that has four departments to manage.
These are sales and purchase department with 120 computers, development department with 50 computers, accounts department with 26 computers and management department with 5 computers.
If the administrator has IP 192.168.1.0/24, how can department wise IPs be allocated?

## Slide 151: Variable Length Subnet Mask (VLSM)
Step 1: For each segment select the block size that is >= the actual requirement. Make a list of subnets possible:

## Slide 152: Variable Length Subnet Mask (VLSM)
Step 2: Arrange all the segments in descending order based on the block size that is from highest to lowest requirement:

## Slide 153: Variable Length Subnet Mask (VLSM)
Step 3: The highest IP available has to be allocated to highest requirement, so the sales and purchase department gets 192.168.1.0/25, which has 126 valid addresses that can easily be available for 120 hosts. The subnet mask used is 255.255.255.128.
Network address: 192.168.1.0
Host range: 192.168.1.1 – 192.168.1.126
Broadcast address: 192.168.1.

## Slide 154: Variable Length Subnet Mask (VLSM)
Step 4: The next segment (Development) requires an IP to handle 50 hosts. We need /26 for 62 hosts. The subnet mask used is 255.255.255.192.
Network address: 192.168.1.128
Host range: 192.168.1.129 – 192.168.1.190
Broadcast address: 192.168.1.191

## Slide 155: Variable Length Subnet Mask (VLSM)
Step 5: Accounts needs 26 hosts. We will need /27, as it has 30 valid hosts. The mask used is 255.255.255.224.
Network address: 192.168.1.192
Host range: 192.168.1.193 – 193.168.1.222
Broadcast address: 192.168.1.223

## Slide 156: Variable Length Subnet Mask (VLSM)
Step 6: The last segment (Management) requires 5 valid hosts IP, which means /29. Subnet mask is 255.255.255.248
Network address: 192.168.1.224
Host range: 192.168.1.225 to 192.168.1.230
Broadcast address: 192.168.1.231

## Slide 157: Summary

## Slide 158: VLSM Example

## Slide 159: VLSM Example – Design Steps
Find the largest segment and allocate a suitable subnet size for it.
Allocate this subnet at the start of the address space.
Continue going down the list.

## Slide 160: VLSM Example – Design Steps
The Engineering departments in both sites have 28 hosts.
For our example we’ve been told that the departments will not grow and we need to use the smallest subnets possible to maximise our address space.
Calculate the optimal subnet mask for the Engineering departments.
Also determine the network and broadcast addresses that will be allocated to both Engineering departments, and the range of host addresses.

## Slide 161: Engineering Departments
We’ve been allocated 200.15.10.0/24

## Slide 162: New York Sales Department
The next largest subnet is New York Sales which requires 14 hosts.
Calculate the optimal subnet mask.
Also determine the network and broadcast addresses that we will allocate, and the range of host addresses.

## Slide 163: New York Sales Department
We’ve been allocated 200.15.10.0/24
New York Sales Department
We’ve been allocated 200.15.10.0/24
/28 (or 255.255.255.240) supports 14 hosts
200.15.10.0 to 200.15.10.63 are already in use by the Engineering departments, so this network address will start at 200.15.10.64
The network address goes up in values of 16, so the next one is 200.15.10.80
Our broadcast address is 200.15.10.79
Valid host addresses are 200.15.10.65 to 200.15.10.78

## Slide 164: Boston Sales Department
The next largest subnet is Boston Sales which requires 7 hosts.
Calculate the optimal subnet mask.
Also determine the network and broadcast addresses that we will allocate, and the range of host addresses.

## Slide 165: Boston Sales Department
We’ve been allocated 200.15.10.0/24
/28 (or 255.255.255.240) supports 14 hosts
/29 does not support 8 hosts! Remember to subtract 2 for the network and broadcast address
200.15.10.0 to 200.15.10.79 are already in use, so this network address will start at 200.15.10.80
The network address goes up in values of 16, so the next one is 200.15.10.96
Our broadcast address is 200.15.10.95
Valid host addresses are 200.15.10.81 to 200.15.10.94

## Slide 166: Are we done?
Don’t forget the links between routers

## Slide 167: New York to Boston Link
The last subnet is the link between the New York and Boston routers.
Calculate the optimal subnet mask.
Also determine the network and broadcast addresses that we will allocate, and the range of host addresses.

## Slide 168: New York to Boston Link
We’ve been allocated 200.15.10.0/24
/30 (or 255.255.255.252) supports 2 hosts
200.15.10.0 to 200.15.10.95 are already in use, so our network address will be 200.15.10.96
The network address goes up in values of 4, so the next one is 200.15.10.100
Our broadcast address is 200.15.10.99
Valid host addresses are 200.15.10.97 to 200.15.10.98

## Slide 169: Summary

## Slide 170: Original Network Diagram

## Slide 171: Diagram with Network Topology

## Slide 172: VLSM Problem
Create VLSM
IP address: 205.15.43.0/24

## Slide 173: Solution
We have 6 networks: LAN1 – LAN2 – LAN3 – WAN link1 – WAN link2 – WAN link3
Order the networks from the largest size to the smallest:
  1) LAN2 (50 hosts)
  2) LAN1 (24 hosts)
  3) LAN3 (8 hosts)
  4) WAN link 1 - WAN link 2 - WAN link 3 (2 hosts each)

## Slide 174: LAN2
Needs 50 hosts, so we will need to use /26 (will give 62 hosts)
Subnet mask: 255.255.255.192
Network address: 205.15.43.0
Host range: 205.15.43.1 - 205.15.43.62
Broadcast address: 205.15.43.63

## Slide 175: LAN1
Needs 24 hosts, so we will need to use /27 (will give 30 hosts)
Subnet mask: 255.255.255.224
Network address: 205.15.43.64
Host range: 205.15.43.65 - 205.15.43.94
Broadcast address: 205.15.43.95

## Slide 176: LAN3
Needs 8 hosts, so we will need to use /28 (will give 14 hosts)
Subnet mask: 255.255.255.240
Network address: 205.15.43.96
Host range: 205.15.43.97 - 205.15.43.110
Broadcast address: 205.15.43.111

## Slide 177: WAN Link1
Needs 2 hosts, so we will need to use /30 (will give 2 hosts)
Subnet mask: 255.255.255.252
Network address: 205.15.43.112
Host range: 205.15.43.113 - 205.15.43.114
Broadcast address: 205.15.43.115

## Slide 178: WAN Link2
Needs 2 hosts, so we will need to use /30 (will give 2 hosts)
Subnet mask: 255.255.255.252
Network address: 205.15.43.116
Host range: 205.15.43.117 - 205.15.43.118
Broadcast address: 205.15.43.119

## Slide 179: WAN Link3
Needs 2 hosts, so we will need to use /30 (will give 2 hosts)
Subnet mask: 255.255.255.252
Network address: 205.15.43.120
Host range: 205.15.43.121 - 205.15.43.122
Broadcast address: 205.15.43.123

## Slide 180: Summary

## Slide 181: Classless Inter Domain Routing (CIDR)

## Slide 182: Problem CIDR Solves
Traditional IP addressing is classful
Available host IP addresses in each class make class C almost unusable, putting great pressure on class A and B:
  Class A - Over 16 million host identifiers
  Class B - 65,535 host identifiers
  Class C - 254 host identifiers
Classful addressing: If a company has more than 254 hosts, it cannot use a class C network, but a class B network would give 65,534 hosts, which was too big! – Result waste of IP address space
Classless Inter Domain Routing (CIDR) uses Variable Length Subnet Mask (VLSM) concept, so it allows subnet masks of variable lengths
A CIDR IP address is classless
Now we can allocate IP address blocks as per the needs (and not as per the class limitations, as mentioned above)

## Slide 183: CIDR Notation
Format: a.b.c.d/n
Here, n = mask or number of bits representing the network id
Example of a CIDR address: 200.10.20.40/28
This is called as the slash notation
Now network id is called as prefix and host id is called as suffix
In the above example, 28 bits represent the network id and 4 bits represent the host id, so 24 - 2 = 14 hosts are possible
Binary mask will be 11111111.11111111.11111111.11110000, decimal mask will be 255.255.255.240
Network id Host id
Prefix Suffix

## Slide 184: CIDR: Finding Network Id
Consider a CIDR address 200.10.20.40/28
Writing the last octet in binary: 200.10.20.00100010/28
Since the slash notation is /28, the first four bits of the last octet are a also part of the prefix – we must not touch them
So, in CIDR:
The network address will be 200.10.20.00100000/28 and in decimal it will be 200.10.20.32/28
The broadcast address will be 200.10.20.00101111/28 and in decimal it will be 200.10.20.47/28
The host range is 200.10.20.33/28 to 200.10.20.46 (14 hosts)

## Slide 185: Rules for CIDR
Addresses should be contiguous
Number of addresses in a block must be power of 2
First address of any block must be evenly divisible by the size of the block

## Slide 186: Example
Is a block of IP addresses 100.1.2.32/28 to 100.1.2.47/28 a valid IP address block?
All the IP addresses are contiguous.
Total number of IP addresses in the Block = 16 = 24.
1st IP address: 100.1.2.00100000/28. Since Host Id will contains last 4 bits and all the least significant 4 bits are zero; the first IP address is evenly divisible by the size of the block.
All three rules are followed by this Block. Hence, it is a valid IP address block.

## Slide 187: Tricky Problem
Do the following two IP addresses belong to the same physical network?
192.168.200.5/30 and 192.168.200.9/30

## Slide 188: Solution
First IP address
Address: 192.168.200.5/30 11000000.10101000.11001000.00000101
Netmask: 255.255.255.252 11111111.11111111.11111111.11111100
4 addresses are possible, including network address and broadcast address
Network: 192.168.200.4/30 11000000.10101000.11001000.00000100
Broadcast: 192.168.200.7 11000000.10101000.11001000.00000111
Host 1: 192.168.200.5 11000000.10101000.11001000.00000101
Host 2: 192.168.200.6 11000000.10101000.11001000.00000110
Hosts/Net: 2

## Slide 189: Solution
Second IP address
Address: 192.168.200.9/30 11000000.10101000.11001000.00001001
Netmask: 255.255.255.252 11111111.11111111.11111111.11111100
4 host address are possible, including network address and broadcast address
Network: 192.168.200.8/30 11000000.10101000.11001000.00001000
Broadcast: 192.168.200.11 11000000.10101000.11001000.00001011
Host 1: 192.168.200.9 11000000.10101000.11001000.00001001
Host 2: 192.168.200.10 11000000.10101000.11001000.00001010
Hosts/Net: 2

## Slide 190: Conclusion
Hosts 192.168.200.5/30 and 192.168.200.9/30 have the same suffix, and yet they do not belong to the same physical network

## Slide 191: CIDR, Route Aggregation and Supernetting
Supernetting is the process of summarizing a number of contiguous subnetted networks back in a single large network
This process is also known as route summarization or route aggregation
Supernetting is mainly done for optimizing the routing tables
Without supernetting, a router will share information about all the routes in its routing table with the other routers
With supernetting, it will summarize them before sharing
Route summarization reduces the size of routing updates dramatically

## Slide 192: Supernetting Example – 8 Subnets Summarized Into One

## Slide 193: Route Summarization Example

## Slide 194: Router and Routing

## Slide 195: Routing: Key Aspects
Routing table
Routing algorithms

## Slide 196: How Routers Learn about Routes?
Default routing
  All routes send packets to a single router
Static routing
  We manually add routes to the routing tables
Dynamic routing
  Routers learn about routes from each other or because of broadcasts

## Slide 197: Interior and Exterior Gateway Protocols

## Slide 198: Classes of Routing Protocols
Distance Vector Protocols (Example: RIP – Routing Information Protocol)
  Use distance to measure the route cost
  The number of hops between the router and a destination network establishes the distance
  Regularly send their whole routing table to the remote routers
  The receiving router then integrates its routing table with the received data based on the metrics
Link State Protocols (Example: OSPF – Open Shortest Path First)
  Form a remote connection with other routers prior to sharing routing data
  They don’t broadcast routing data to the whole network
Path Vector Protocols (Example: BGP – Border Gateway Protocol)
  Works across interior networks, i.e. in an exterior network

## Slide 199: Routing Information Protocol (RIP)
RIP routers use only routing tables to store information
RIP can store multiple routes to the same destination and uses as its metric a value called hop count
Hop count is the number of routers that are in the path to the destination network using that route
Broadcasts UDP data packets to exchange routing information
Cisco software sends routing information updates every 30 seconds, which is termed advertising
If a device does not receive an update from another device for 180 seconds or more, the receiving device marks the routes served by the non updating device as unusable
If there is still no update after 240 seconds, the device removes all routing table entries for the non updating device

## Slide 200: Distance Vector Routing Example – Step 1

## Slide 201: Distance Vector Routing Example – Step 2

## Slide 202: Distance Vector Routing Example – Step 3
More updates will be needed to fill the blanks/gaps …

## Slide 203
Variations of RIP: IGRP and EIGRP
The Interior Gateway Routing Protocol (IGRP) is a distance-vector routing protocol.
IGRP has been superseded by Enhanced IGRP (EIGRP), which has many new features.
IGRP and EIGRP have a compound metric that takes into account several factors, such as link bandwidth and latency.
As such, IGRP is superior to RIP, which takes into account only the hop count, and RIPv2, which uses both hop count and bandwidth.
In addition to the compound metric, which allows better route selection, IGRP tends to have better convergence times, meaning that routing stabilizes more quickly after a network disruption.
Notes: 203

## Slide 204
Drawbacks
IGRP and EIGRP are proprietary protocols, which means they are implemented only by Cisco routers.
IGRP (like RIP) broadcasts the entire routing table, which can consume a lot of network bandwidth
Notes: 204

## Slide 205
IGRP versus EIGRP
EIGRP supports VLSM, IGRP does not
Path calculations are improved in EIGRP
EIGRP has less frequent updates as compared to IGRP
Notes: 205

## Slide 206: OSPF
Open Shortest Path First (OSPF) is an industry-standard protocol that operates on non-Cisco routers also
Based on link-state routing
Detailed routing information about an area is confined to that area, and only a summary of information is advertised to other areas
This has the benefit of keeping OSPF routing tables smaller
RIP works fine in small networks, but not in large networks
When routers exchange information, it is called as flooding
Frequency of exchange is once in every 1-2 hours

## Slide 207: OSPF Area

## Slide 208: Understanding OSPF
Two aspects: OSPF tables and OSPF packets
OSPF uses three tables
  Neighbor Table: Information about neighbors
  Topology Table: Information about other routers and networks in the AS
  Routing Table
It uses five packets
  Hello Packets
  Database Descriptor (DBD)
  Link State Request (LSR)
  Link State Update (LSU) – Most important
  Link State Acknowledgement (LSAck)

## Slide 209: Link State Update Packet
Main packet, used by a router to advertise the state of its links
Format

## Slide 210: Link State Update – Example
What will be the LSA part of the Link State Update packet sent by router 10.24.7.9?

## Slide 211: Link State Update – Example
1: It is about a router
3: It is about a network

## Slide 212: Flooding into the Neighbouring Areas

## Slide 213: Path Vector Routing – Step 1
Each AS has at least one path vector routing that collects reachability information for each network in that AS

## Slide 214: Path Vector Routing – Step 2
A path vector routing table for each router can be created if ASs share their reachability list with each other

## Slide 215: Network Address Translation (NAT)

## Slide 216: Network Address Translation (NAT) Concept

## Slide 217: NAT Mapping Example

## Slide 218: InfiniBand Network

## Slide 219: InfiniBand Network
InfiniBand is an open standard network interconnection technology with high bandwidth, low delay and high reliability
This technology is defined by IBTA (InfiniBand Trade Alliance)
This technology is widely used in HPC
Supports basic Single Data Rate (SDR) of 2.5 Gbps
Usually, four cables are used together, to geta speed of 10 Gbps
Another improvement called as Quad Data Rate (QAD) signaling takes this rate to 40 Gbps
Significant advantages over Ethernet and optical fiber

## Slide 220: InfiniBand Basics
Traditionally, I/O was handled by the shared PCI bus (32 or 44 bit transfer)
In InfiniBand, the I/O is handled not by processors, but by interconnect architecture
This means that the I/O does not go to the kernel area of the operating system, but directly comes in to or goes out from the user area
Makes it very fast
Packets are of 4 KB